## Slide 1
802.11 Technology, Wi-Fi Basics
-Layered architecture, Modulation/coding overview

## Slide 2
Contents
1.OSI 7-layer architecture
2.802.11 within OSI framework
3.Wi-Fi standards
4.Data link layer in action
5.Physical layer in action
6.802.11 Working group
7.Wi-Fi 2.4 GHz Channels
8.Wi-Fi 5 GHz channels
9. 802.11 Coding & Modulation schemes
10.DSSS coding & modulation
11. OFDM coding & modulation
12. Quadrature Amplitude Modulation

## Slide 3
Open Systems Interconnection model (OSI) -Overview
Data bits logically arranged, encoded before sent through a media.
Packets into Frames (Packet + MAC address of sender/Receiver
Data Frames are read & physical addresses added
IP addresses on segments,
Short Path determination
Segments encapsulated, routing packets to terminal
data segmentation
Flow control, error control
TCP,UDP : with/without feedback
Establish connection
& session management
authentication, authorization
Data to common format
ASCII to EBCDIC
Email, s/w programs
User interaction window
Translation, compression, encryption
Frames to bits and sent over the n/w thru a media
Heart of OSI
Developed by International Standards organization in the year 1984
Basis for networking to support interoperability between different products and software.

## Slide 4
2.4GHz DSSS ,OFDM
5GHz DSSS ,OFDM
6GHz DSSS ,OFDMA
802.11 protocol within OSI framework
802.11 is a set of Data link and Physical layer protocols
Mac layer is responsible for reliable link to link data transfer (Channel access, addressing, frame validation, error detection, security mechanisms
Physical layer is responsible for data transfer through a media (Cable/Light/Wireless

## Slide 5
Logic Link control(LLC)
Medium Access Control(MAC)
Data Link
Layer
Physical
Layer
802.11
FHSS
802.11b
DSSS
802.11a
OFDM
802.11g
OFDM
802.11n
OFDM
MIMO
802.11ac
OFDM
MIMO
802.11ax
OFDMA
MUMIMO
Wi Fi standards , Data link & Physical layer
Wi-Fi is a trade mark owned by Wi-Fi alliance and it is a collection of protocols that replace Ethernet cables

## Slide 6
Data Link layer–Access to media and control scenario
LLC Linking upper host layers to access media (Cable/Optical/Wireless) through frames
Controls how data is placed and received from the media through Media Access Control- CSMA and Error detection ( Tail bits in the frame are for error detection)

## Slide 7
Physical layer in action – A big picture
Data frame received from DLC layer is a sequence of bits ((1’s and 0’s)
Bit sequence is converted to signal and transmit over local media (Ethernet/Fiber/Wireless)

## Slide 8
802.11ax (9.6Gbps)
802.11 Work groups

## Slide 9
2.4GHz band Wi-Fi Channels

## Slide 10
5GHz band Wi-Fi Channels

## Slide 11
802.11 (oldest standard-1997)
Spread spectrum method
802.11 Coding &Modulation schemes

## Slide 12
DSSS Coding and Modulation Cont’d
Transmit spread spectrum
Complementary Code keying (CCK)
Rx De-spreading

## Slide 13
BPSK,QPSK Modulation schemes
BPSK
QPSK
Constellation for BPSK,QPSK

## Slide 14
OFDM Multicarrier Scheme
Orthogonal sub carriers
5 GHz Channels
64 sub carriers 20MHz BW

## Slide 15
OFDM modulation format and advantages

## Slide 16
Quadrature Amplitude Modulation (QAM)
8 QAM
This system uses 4 possible phase angles and 2 possible amplitudes
Constellation shows 8 symbols along with 3 bits digital words
OFDM modulation & code rates

## Slide 17
Later : OFDM Implementation

## Slide 18
OFDM generation & Serial to parallel and Parallel to serial (IFFT/FFT) conversion

## Slide 19
802.11N/AC specific details and comparison