## Slide 1
802.11 Technology, Wi-Fi Basics
-Layered architecture, Modulation/coding overview

## Slide 2
Contents
1.OSI 7-layer architecture
2.802.11 within OSI framework
3.Wi-Fi standards
4.Data link layer in action
5.Physical layer in action
6.802.11 Working group
7.Wi-Fi 2.4 GHz Channels
8.Wi-Fi 5 GHz channels
9. 802.11 Coding schemes
10. PSK & QAM Modulation
11. OFDM scheme and implementation
12. 802.11n standard and maximum data rate

## Slide 3
Open Systems Interconnection model (OSI) -Overview
Data bits logically arranged, encoded before sent through a media.
Packets into Frames (Packet + MAC address of sender/Receiver
Data Frames are read & physical addresses added
IP addresses on segments,
Short Path determination
Segments encapsulated, routing packets to terminal
data segmentation
Flow control, error control
TCP,UDP : with/without feedback
Establish connection
& session management
authentication, authorization
Data to common format
ASCII to EBCDIC
Email, s/w programs
User interaction window
Translation, compression, encryption
Frames to bits and sent over the n/w thru a media
Heart of OSI
Developed by International Standards organization in the year 1984
Basis for networking to support interoperability between different products and software.

## Slide 4
2.4GHz DSSS ,OFDM
5GHz DSSS ,OFDM
6GHz DSSS ,OFDMA
802.11 protocol within OSI framework
802.11 is a set of Data link and Physical layer protocols
Mac layer is responsible for reliable link to link data transfer (Channel access, addressing, frame validation, error detection, security mechanisms
Physical layer is responsible for dta transfer through a media (Cable/Light/Wireless

## Slide 5
Logic Link control(LLC)
Medium Access Control(MAC)
Data Link
Layer
Physical
Layer
802.11
FHSS
802.11b
DSSS
802.11a
OFDM
802.11g
OFDM
802.11n
OFDM
MIMO
802.11ac
OFDM
MIMO
802.11ax
OFDMA
MUMIMO
Wi Fi standards , Data link & Physical layer
Wi-Fi is a trade mark owned by Wi-Fi alliance and it is a collection of protocols that replace Ethernet cables

## Slide 6
Data Link layer–Access to media and control scenario
LLC Linking upper host layers to access media (Cable/Optical/Wireless) through frames
Controls how data is placed and received from the media through Media Access Control- CSMA and Error detection ( Tail bits in the frame are for error detection)

## Slide 7
Physical layer in action – A big picture
Data frame received from DLC layer is a sequence of bits ((1’s and 0’s)
Bit sequence is converted to signal and transmit over local media (Ethernet/Fiber/Wireless)

## Slide 8
802.11ax (9.6Gbps)
802.11 Work groups

## Slide 9
2.4GHz band Wi-Fi Channels

## Slide 10
5GHz band Wi-Fi Channels

## Slide 11
802.11 (oldest standard-1997)
Spread spectrum method
802.11 Coding schemes

## Slide 12
DSSS Coding Cont’d
Transmit spread spectrum
Complementary Code keying (CCK)
Rx De-spreading

## Slide 13
Quadrature Amplitude Modulation (QAM)
8 QAM
This system uses 4 possible phase angles and 2 possible amplitudes
Constellation shows 8 symbols along with 3 bits digital words
OFDM modulation & code rates

## Slide 14
BPSK,QPSK Modulation schemes
BPSK
BPSK Spectrum
Prefiltered Filter to
confine main lobe
Raised cosine pulse shape
to confine main lobe
QPSK Spectrum
QPSK

## Slide 15
OFDM Multicarrier Scheme
Orthogonal sub carriers
OFDM makes use of many closely spaced orthogonal subcarriers that are transmitted in parallel
Each subcarrier is modulated with a conventional digital modulation scheme (such as BPSK,QPSK, 16QAM, etc.)
combination of many subcarriers enables data rates like conventional single-carrier modulation schemes within equivalent bandwidths
Why OFDM?
High spectral efficiency :Bits/Hz
Resilient to frequency selective fading & narrow band interference
Immunity towards Multi path fading resulting in Inter Symbol Interference(ISI)

## Slide 16
OFDM modulation format and advantages

## Slide 17
Typical OFDM burst in 802.11
The Preamble with known amplitude and phase is used for synchronization and channel equalization.
The SIGNAL field is transmitted using BPSK, and contains the length, modulation type, and data rate information.
Multiple OFDM symbols containing the input data bits are appended to complete the burst.

## Slide 18
OFDM generation
802.11a Burst signal spectrum
802.11a Burst signal timing parameters
OFDM Implementation
OFDM Transmitter & receiver

## Slide 19
FFT ,IFFT and OFDM TX/RX
FFT decomposes a given signal
FFT and IFFT are fast computational algorithms for FT and Inverse FT which can be implemented efficiently in Digital signal processing (DSP)
OFDM transmitter and Receiver
FFT Decomposes an N point time domain signal into N time domain signals each composed of a single point.
Calculate the N frequency spectra corresponding to these N time domain signals. Lastly, the N spectra are synthesized into a single frequency spectrum.

## Slide 20
20MHz OFDM uses an FFT of size 64 and the FFT period =3.2uS and guard is 0.8uS
A symbol period of T=4μs which corresponds to 250kbits/s on a single carrier BPSK
Multicarrier of 48 subcarriers BPSK within 4μs increases the bit rate to 12 Mb/s
Multicarrier of 48 subcarriers QPSK within 4μs increases the bit rate to 24 Mb/s
Change amplitude and the phase of the sine wave(16QAM), increases rate to 48Mb/s
64QAM uses 6 bits per subcarrier (2^6=64) resulting in 72 Mbps data rate
256QAM uses 8 bits per subcarrier (2^8=256) resulting in 96 Mbps data rate
1024QAM uses 10 bits per subcarrier (2^10=1024) resulting in 120 Mbps data rate
Wider channel BW increases data capacity linearly : 40MHz/80MHz/160MHz
MIMO system further increase data rate: SISO rate x Number of spatial streams
Higher modulations & MIMO for Higher spectral efficiency
802.11b data rates: 1,2,5,11Mb/s –SISO -> Known as DSSS
802.11a/g data rates : 6,9,12,18,24,36,48,54 -> Known as OFDM
802.11n data rates : 600Mb/s (64QAM, 40MHz/4x4 MIMO )-> Known as HT
802.11ac data rates: 6.933Gb/s (256 QAM/160MHz/8x8 MIMO) -> VHT
Max Data rate =( Data carriers x Spatial stream x Bits/symbol x Code rate) /Symbol duration

## Slide 21
Modulation & Coding (MCS) and 802.11n
802.11n/ac use the term MCS – Multiple combinations of spatial streams , modulation type, coding rate yield same data rate
MCS index for 802.11n extends from MCS 76 to MCS 0 (E.g.: MCS33 ->16QAM for stream 1 and QPSK for stream 2
802.11ac MCS index is from MCS0 to MCS9
Unequal modulations are not supported in 11Ac
Number of data carriers =52 (48 for a/g)
Max MIMO channels =4 (SISO for a/g)
Max channel Bandwidth =40MHz ( 20MHz in a/g)
Symbol duration ,Guard Interval = 3.6uS , 400nS (800nS in a/g)
Highest order modulation scheme = 256QAM ( 64 QAM in a/g)
Code rate =5/6 (For 5 data bits, a total of 6 are transmitted)
N point FFT =128 ( 64 in a/g)
Max data rate = (108x4x8x5/6)/3.6uS=600Mb/s
802.11n changes with respect to 802.11a/g

## Slide 22
Flip side of higher modulation scheme is on sensitivity performance
Sensitivity S = 10lg(kTB) + NF + SNR
= -174dBm/Hz + 73dBm(20MHz,BW)+5dB+3dB
=-93dBm
Typical SNRs with higher modulation schemes
SNR(QPSK)
NF
OFDM with higher modulation: performance
SNR
Sensitivity requirement for the receiver changes with error performance requirements., Say for example 5%/10 frames in error